## Slide 1: RECAP SW 6 (Lesson 27.10.2017)
Florian Lussi und Thomas Elmiger

## Slide 2: Hooks
Concept: hooks are used as events to notify the application
Hooks are optional
Error hooks: disable interrupts and halt system

## Slide 3: Idle Hook
Called from the IDLE task, whenever the system no user task is running
Ideal place to go into low power mode
Toggle LED/Pin: activity shows idle activity ) Low Power
I Idle hook function not allowed to call blocking API functions!

## Slide 4: Tick Hook
Called from tick interrupt
Can be used instead of a dedicated timer running at tick frequency
Executed in interrupt context, keep it short!
Only FromISR() RTOS API functions can be called

## Slide 5: Malloc Failed Hook
Called if memory allocation failed

## Slide 6: Stack Overflow Failed Hook
Method 1: Check SP at task swap time
Method 2: Method 1 + checking last 16 bytes pattern

## Slide 7: Questions
What is a easy way to detect the active Time of the Idle Task?

## Slide 8: Questions
What is a simple way to detect the active Time of the Idle Task?
Toggle LED/Pin: activity shows idle activity

## Slide 9: Questions
Do you have to use Hooks?

## Slide 10: Questions
Do you have to use Hooks?
No